## Slide 1: The classification of GPR signals using Keras
Przemek Dolowy
HARUG
April 2022

## Slide 2
Water content
Relative dielectric permittivity (εr) of the scanned material
reflection wherever there is a change of εr
attenuation (frequency selective)
scattering on sub-wavelength structures
overlapping reflections create interference frequencies
Soil texture
GROUND PENETRATING RADAR – WHY IT MIGHT DETECT SOIL COMPACTION
Vertical distribution of soil moisture
Layers of compacted soil
Presence of objects and voids
Soluble salts
Scanning height
Radar frequency
Radar specs
Mineralogical composition
Crop growth

## Slide 3
EARLIER RESULTS

## Slide 4
EXPERIMENTAL SITE STRUCTURE
W – wheelway
C – centre
plot width (ca 4 m)

## Slide 5
GROUND PENETRATING RADAR (GPR)
STATIC SCANNING OF THE FIELD EXPERIMENTAL SITES
Scanning the New Hopyard experimental site (April 2021)
Number of scans in the datasets
Large Marsh 1 – 440
New Hopyard 1 – 480
Large Marsh 2 – 858
New Hopyard 2 – 930

## Slide 6
LABELS TO PREDICT WITH KERAS
Label | Values | Comment
Zone | W – wheelway C – Centre | Crop rows 4-7 Crop rows 10-13
Traffic Contrast | HT – High Traffic LT – Low Traffic | 0-1 wheel passes annually 2-4 wheel passes annually
Tillage Depth | D – Deep S – Shallow Z – Zero | 250 mm 100 mm Zero tillage
Tyre Pressure | H – Standard (High) L – Low | 
Block | 1, 2, 3, 4 | 
Moisture Contrast | HMC – High LMC – Low | Soil water content threshold depending on site

## Slide 7
Static GPR scan in a proprietary GSF format
Data handling and pre-processing scripts
import: GSF >> SGY >> CSV
stacking
labelling (attaching information)
A time-domain dataset in CSV format, row-wise,
1 averaged trace per scan
data labels (site, date, plot number, position, treatments, and so on)
Field notes from scanning
DATA ACQUISITION AND PRE-PROCESSING
Site structure:
- experimental factors on plots,
- trafficking pattern
Soil moisture data

## Slide 8
n averaged traces in a dataset
256 samples / trace (32 ns x 8 samples/ns)
Decimal range:
from -32768 to 32767
an example of a trace
A TIME-DOMAIN DATASET STRUCTURE

## Slide 9
FEATURE VECTORS FOR CLASSIFICATION
3 options:
TD - a selected section of the time-domain signal
FT - a spectrum of a selected section of the time-domain signal
SA - a set of signal attributes calculated from the time-domain signal or/and the spectrum

## Slide 10
A selected setion of a time-domain trace
Discrete Fourier Transform
Amplitude spectrum
Power spectrum
Squaring
Time-domain-based signal attributes (7)
Amplitude spectrum-based signal attributes (9)
Power-spectrum-based signal attributes (4)
Signal attributes
HOW THE SIGNAL ATTRIBUTES ARE CALCULATED...
1) TD
2) FT
3) SA

## Slide 11
Signal attributes - raw
Z-normalisation: Z = (X – mean of X) / standard deviation of X
(in R: Z = scale(X) )
where X is the raw value of a given signal attribute
Signal attributes – Z-norm
Signal attributes – Logistic
Logistic transform: L = (100/(1+exp(-0.5*Z)))
... AND NORMALISED
Features for Keras

## Slide 12
Dataset
ModelMasterLooped
make a settings list
PROCESSING FLOW
Settings (manual input)
ModelData
read in and sub-select data
CLASSES vector
FEATURES matrix
ModelTrainAndTest
split CLASSES and FEATURES into training and test sets
define and compile the KERAS model
train and evaluate the model
generate predictions on test data
generate confusion matrix
save the trained model and settings
ModelStats
pre-eavaluation of features (optional)
pre-evaluated features
boxplots (optional)
corrplot
ModelReport
output a summary and barplots
passed to further stages
output to save

## Slide 13
DISTRIBUTION OF THE FEATURES

## Slide 14
DISTRIBUTION OF THE FEATURES

## Slide 15
DISTRIBUTION OF THE FEATURES

## Slide 16
DISTRIBUTION OF THE FEATURES

## Slide 17
DISTRIBUTION OF THE FEATURES

## Slide 18
DISTRIBUTION OF THE FEATURES

## Slide 19
DISTRIBUTION OF THE FEATURES

## Slide 20
CORRELATION BETWEEN THE FEATURES

## Slide 21
Model performance was assessed using total accuracy.
A = correctly assigned labels / total number of classified examples
additionally:
- precision (by class)
P = correct predictions of class X to the overall number of predictions of class X
- recall (by class)
R = correct predictions of class X / all occurences of class X in the dataset
ASSESSMENT OF MODEL PERFORMANCE

## Slide 22
RUN 1

## Slide 23
RUN 2

## Slide 24
Detection of soil characteristics with GPR is possible
Soil moisture is likely to be the main factor…
…and a proxy to detect agricultural traffic
CONCLUSIONS
Tweaks to the Keras model structure
Pre-processing, filtering…
Depth selection
Tweaks to the selection of attributes
New attributes?
More data!
Quick data collection in mobile mode with sufficient positioning precision
HOW TO MAKE IT WORK BETTER

## Slide 25
Thank you!